## Slide 1: OpenSMART: Single-cycle Multi-hop NoC Generator in BSV and Chisel
April 25, 2017
Georgia Institute of Technology
Synergy Lab (http://synergy.ece.gatech.edu)
hyoukjun@gatech.edu
Hyoukjun Kwon and Tushar Krishna

## Slide 2: Hardware Development Cost
source: Todd Austin, Micro-49 keynote
Low cost challenge
Notes: There has been no culture of IP reuse because companies try to squeeze as much performance as possible by reimplmeneting each IP for specific systems

## Slide 3: Many-IP Heterogeneous System
Scalability challenge
Network-on-Chip
(NoC)
Flexibility challenge

## Slide 4: Diverse System Requirements
source: MNIST, Engadget, TheStack
Throughput Critical
Latency Critical

## Slide 5: Challenges for NoCs
Low-cost
  Low design/verification costs of custom/generic NoCs
  Design automation of high-performance, low-energy NoCs
Scalability
  Many-IP heterogeneous system support
  Low latency
  Low energy
  Low area
Flexibility
  Diverse connectivity
  Diverse latency/throughput requirements

## Slide 6: OpenSMART
OpenSMART

## Slide 7: Outline
Motivation: Scalable, Flexible, and Low-cost NoCs
Background: SMART NoCs
OpenSMART
  Design Flow
  Building Blocks
  Walk-through Examples
Case Studies
  Mesh vs. SMART
  High-radix vs. Low-radix
Conclusions

## Slide 8: Outline
Motivation: Scalable, Flexible, and Low-cost NoCs
Background: SMART NoCs
OpenSMART
  Design Flow
  Building Blocks
  Walk-through Examples
Case Studies
  Mesh vs. SMART
  High-radix vs. Low-radix
Conclusions

## Slide 9: SMART NoC
1-cycle (no other traffic)
Krishna et al, HPCA 2013
Chen et al, DATE 2013
Krishna et al, IEEE Micro Top Picks 2014,
S
D
HPCmax
SSR (SMART Setup Request)
SSR (SMART Setup Request)
SSR (SMART Setup Request)
Single-cycle Multi-hop Asynchronous Repeated Traversal
SMART: achieves the performance of dedicated connections over a network of shared links

## Slide 10: Is 1-cycle Network Possible?
~20mm
~20mm
~20mm
~20mm
Is wire fast enough to support 1-cycle network?
Wire traversal length within 1ns (1Ghz): 10-16mm
Wire delay over technology: constant
Chip dimension: remain similar (~20mm)
Clock frequency: remain similar (1~3GHz)
Tile dimension: decrease over technology
On-chip wires are fast enough to transmit across the chip within 1-2 cycles at 1GHz even if the technology scales
Yes
Notes: Repeaters are just Inverters and buffers. The knwon fact is that 70~80 ps is reuiqred to traverse 1mm with global repeated wires

## Slide 11: Features of SMART
Low latency network
  Dynamic bypass of intermediate routers between any two routers
  Limit: HPCmax (hops per cycle max), maximum number of “hops” that the underlying wire allows the flit to traverse within a clock cycle
Separate control path
  HPCmax bits from every router along each direction
  Arbitration of multiple bypass requests on the same link
  No ACK required

## Slide 12: Outline
Motivation: Scalable, Flexible, and Low-cost NoCs
Background: SMART NoCs
OpenSMART
  Design Flow
  Building Blocks
  Walk-through Examples
Case Studies
  Mesh vs. SMART
  High-radix vs. Low-radix
Conclusions

## Slide 13: OpenSMART Design Flow

## Slide 14: OpenSMART NoC

## Slide 15: Outline
Motivation: Scalable, Flexible, and Low-cost NoCs
Background: SMART NoCs
OpenSMART
  Design Flow
  Building Blocks
  Walk-through Examples
Case Studies
  Mesh vs. SMART
  High-radix vs. Low-radix
Conclusions

## Slide 16: OpenSMART Building Blocks
input buffer + input VC arbitration
output VC selection + output port arbitration
+ credit management
switching (via crossbar) + routing calculation
SSR communication & arbitration + bypass flag

## Slide 17: OpenSMART Router
Number of VCs/VC Depth
Flit Size
Arbiter

## Slide 18: OpenSMART Router
Arbiter

## Slide 19: OpenSMART Router
Routing
Algorithm

## Slide 20: OpenSMART Router (SMART)
SSR Prioritization
HPCmax
Prioritization by distance
-> SSR from a nearer router gets the higher priority
(Local (distance = 0) has the highest prirority)
Notes: - Slide 25: Here 2 points should come out when you speak. One: the SSR traversal - put a red circle there and talk about SSRs going up to HPCmax as you've done now. Two: the SSR priority. So show a red circle over that box and say that SSRs are prioritized by distance, with local getting highest priority. And say you will show this with example later.

## Slide 21: OpenSMART Router (1cycle)
Cycle 0
Cycle 1

## Slide 22: OpenSMART Router (2cycle/SMART)
Cycle 0
Cycle 1
Cycle 3

## Slide 23: Outline
Motivation: Scalable, Flexible, and Low-cost NoCs
Background: SMART NoCs
OpenSMART
  Design Flow
  Building Blocks
  Walk-through Examples
Case Studies
  Mesh vs. SMART
  High-radix vs. Low-radix
Conclusions

## Slide 24: Walk-through Example 1
Router r4 sends a flit to router r7
HPCmax = 3
SSR (SMART Setup Request)
Cycle 0: SSR Send
Cycle 1: Multi-hop Bypass
110
110
110
bypass, bypass, stop

## Slide 25: Walk-through Example 2
Router r4 sends a flit to router r7
Router r5 sends a flit to router r7
HPCmax = 3
SSR (SMART Setup Request)
Cycle 0: SSR Send
Cycle 1: Multi-hop Bypass
110
110
110
100
100
SMART Unit in r5
Winner
Notes: - Slide 30 is the only one that shows a contention scenario so needs to be explained well. This is a crucial slide in my opinion. In the animation, once the SSR is sent, show a pop out from r5 showing the hasSSR and has Local Flit blocks and the priority arbiter setting the flag to Red. Emphasize that the arbiter is a simple arbiter that prioritizes SSRs based on distance.

## Slide 26: OpenSMART: Features
Language
  BSV and Chisel
Flow control
  VC and SMART
Buffer management
  Credit-based buffer management
Router microarchitecture
  1- and 2-cycle state-of-the-art packet switching router
  SMART router
Notes: We provide scalable NoC generator that supports irregular topologies

## Slide 27: OpenSMART: Features
Routing calculation
  XY, YX, and source-routing
  One-hot encoding hop count + shift-based routing calculation
  For SMART, routing calculation is done during bypasses
VC selection
  FIFO-based dynamic VC selection
  Next VC is stored in a separate register
  For SMART, VC selection is done during bypasses
Notes: We provide scalable NoC generator that supports irregular topologies

## Slide 28: Outline
Motivation: Scalable, Flexible, and Low-cost NoCs
Background: SMART NoCs
OpenSMART
  Design Flow
  Building Blocks
  Walk-through Examples
Case Studies
  Mesh vs. SMART
  High-radix vs. Low-radix
Conclusions

## Slide 29: Case Study Configuration
Network Topology: 8x8 mesh
Number of VCs: 4
Traffic: Uniform-random and bit-complement
HPCmax : 7
Flit Size : 52 bit (data: 32 bit)
Synthesis Environment : Synopsys Design Compiler with NanGate 15nm PDK standard cell library // Xilinx Vivado (target: VC709 board)
Simulation Method: Cycle-accurate RTL simulation using BSV testbench and Garnet simulation
Notes: We provide scalable NoC generator that supports irregular topologies

## Slide 30: Latency
(a) Uniform Random
(b) Bit-complement
4X
5X

## Slide 31: Energy Consumption
Repeaters require less energy than clocked latches
Notes: Anticipated Question: How did you estimate the energy?

## Slide 32: HPCmax
(a) HPCmax on ASIC
(b) HPCmax on FPGA
Notes: Depends on operating clock frequency and tecnhologies

## Slide 33: Outline
Motivation: Scalable, Flexible, and Low-cost NoCs
Background: SMART NoCs
OpenSMART
  Design Flow
  Building Blocks
  Walk-through Examples
Case Studies
  Mesh vs. SMART
  High-radix vs. Low-radix
Conclusions

## Slide 34: Router Area

## Slide 35: Router Power
(a) ASIC
(b) FPGA
Number of Ports

## Slide 36: Maximum Clock Frequency

## Slide 37: Outline
Motivation: Scalable, Flexible, and Low-cost NoCs
Background: SMART NoCs
OpenSMART
  Design Flow
  Building Blocks
  Walk-through Examples
Case Studies
  Mesh vs. SMART
  High-radix vs. Low-radix
Conclusions

## Slide 38: Conclusion
NoCs are crucial components to support many-IP heterogeneous systems
OpenSMART provides automatic generation of NoCs RTL for many-IP heterogeneous systems
OpenSMART generates not only state-of-the-art packet switching network but also low latency network, SMART.
Thank you!

## Slide 39: Paper and Source code
Paper is available this link : http://synergy.ece.gatech.edu/wp-content/uploads/sites/332/2017/03/OpenSMART_ISPASS17.pdf
Source code is available via this link: https://hyoukjun.github.io/OpenSMART/